## Slide 1: Execution Flow in GridDyn
GridDyn Documents
Philip Top

## Slide 2: Outline
Execution Flow
GridDyn Operational States
Executable: GridDynMain
  Options and control
  File Types
Simple power flow XML example
  File Read and model construction
  Power flow initialization
  Power Flow
Simple Dynamic XML example
  Dynamic Initialization
  Dynamic Calculation
  Output

## Slide 3: Execution Flow: States in GridDyn
Startup
Unloaded or loaded and not initialized
Initialized
Successfully completed powerflow initialization
PowerFlow Complete
Dynamic Initialized
Successfully completed dynamic initialization
Dynamic Complete
Dynamic Partial
Solver Unable to continue on its own
Halted
Not really used
May be removed
Error
Unrecoverable error
Initialize
powerflow
initialize
Dynamic
solve

## Slide 4: GridDynMain
Does two things
  Run a simulation
  Load a simulation and spit out some information (MPI count, counts, help, version, etc)
./gridDynMain [arguments] filename
Common arguments
  --flags=[gridDynFlags] //any flags used by gridDyn
  --powerflow-output=[filename] //save the powerflow results to a file[csv, binary, xml?]
  --powerflow-only //only run the power flow
  -- help
  --param ParamName=<val> //setting simulation parameters(TODO)
  --dir= add a search directory for input files
  --script = script file // [TO BE ADDED] but will allow scripting of griddyn actions and outputs

## Slide 5: GridDynMain: Process
Setup
Load sub libraries
Create the root simulation object
load
Process arguments (settings, flags, parameters, files, definitions)
Load input files (by main input argument or import statements)
Run
Run the simulation (unless told not to)
Parse arguments
Cleanup
Generate any extra output
Cleanup any libraries

## Slide 6: Loading files: though gridDynRunner
Available File Type:
  Cdf: common data format
  Raw/dyr : pss/e files
  PTI : old pss/e files before it was bought by Seimens
  Csv : data entry in a csv file (pretty flexible) useful when you have a lot of objects
  Uct : Eurostag files
  EPC: PSLF files
  M files : both matpower, matdyn and PSAT files
  PSP :: some other format
  XML Most flexible input designed around Griddyn. Not intended to be used elsewhere
    Common use is to load most data through another file type and put the extra custom stuff in through XML.
  Other potential inputs get built as need arises (ODM, CIM, JSON, AUX, etc)

## Slide 7: 2 Bus Example
0.45+j0.2
1.15+j0.31
V=1.05
A=0 deg
Line properties
R=0.0839
X=0.51833
B=0.127
P=?
Q=?
V2=?
A2=?

## Slide 8: Input File in XML
<?xml version="1.0" encoding="utf-8"?>
<griddyn name="2bus_test" version=“1">
<bus name="bus1">
<type>SLK</type>
<angle>0</angle>
<voltage>1.05</voltage>
<generator name="gen1">
</generator>
<load name="load1">
<P>1.05</P>
<Q>0.31</Q>
</load>
</bus>
<bus name="bus2">
<load name="load2">
<P>0.45</P>
<Q>0.2</Q>
</load>
</bus>
…
…
<link from="bus1" name="bus1_to_bus2" to="bus2">
<b>0.127</b>
<r>0.0839</r>
<x>0.51833</x>
</link>
<flags>powerflow_only</flags>
</griddyn>

## Slide 9: Input File in XML
<?xml version="1.0" encoding="utf-8"?>
<griddyn name="2bus_test" version=“1">
<bus name="bus1">
<type>SLK</type>
<angle>0</angle>
<voltage>1.05</voltage>
<generator name="gen1">
</generator>
<load name="load1">
<P>1.15</P>
<Q>0.31</Q>
</load>
</bus>
<bus name="bus2">
<load name="load2">
<P>0.45</P>
<Q>0.2</Q>
</load>
</bus>
…
…
<link from="bus1" name="bus1_to_bus2" to="bus2">
<b>0.1273164</b>
<r>0.083931984</r>
<x>0.518336712</x>
</link>
<flags>powerflow_only</flags>
</griddyn>
XML and test case information
Define Bus 1 with generator and load
SLK to fix the angle and voltage
Define Bus 1 with generator and load
SLK to fix the angle and voltage

## Slide 10: Input File in XML
<?xml version="1.0" encoding="utf-8"?>
<griddyn name="2bus_test" version=“1">
<bus name="bus1">
<type>SLK</type>
<angle>0</angle>
<voltage>1.05</voltage>
<generator name="gen1">
</generator>
<load name="load1">
<P>1.15</P>
<Q>0.31</Q>
</load>
</bus>
<bus name="bus2">
<load name="load2">
<P>0.45</P>
<Q>0.2</Q>
</load>
</bus>
…
…
<link from="bus1" name="bus1_to_bus2" to="bus2">
<b>0.1273164</b>
<r>0.083931984</r>
<x>0.518336712</x>
</link>
<flags>powerflow_only</flags>
</griddyn>
Define the Link between bus1 and bus2
Any additional simulation information

## Slide 11: Execution
./griddynMain two_bus_example.xml --powerflow-output=twobusout.csv
Output on Screen
area count =0 busses=2 links= 1 gens= 1
(startup)[sim]::GridDyn version 0.50 2016-2-10
(startup)[sim]::Initializing Power flow to time -0.001000
(-0.001)[sim]::saving csv powerflow to twobusout.csv
Simulation GridDynSimulation executed in 0.0075812 seconds
simulation final Power flow statesize= 4, 10 non zero elements in Jacobian

## Slide 12: Solution output
basepower=100.000000 |  |  |  |  |  |  |  |  |  | 
Area # | Bus # | Bus name | voltage(pu) | angle(deg) | Pgen(MW) | Qgen(MW) | Pload(MW) | Qload(MW) | Plink(MW) | Qlink(MW)
0 | 1 | "bus1" | 1.05 | 0 | -162.377 | -53.607 | 115 | 31 | 47.3769 | 22.6065
0 | 2 | "bus2" | 0.891033 | -13.6449 | 0 | 0 | 45 | 20 | -45 | -20
Which happens to match the solution in the textbook I took this problem from:
Electric Energy Systems Theory by Olle Elgerd 2nd Edition Example 7-7

## Slide 13: 2 Bus Example
0.45+j0.2
1.15+j0.31
V=1.05
A=0 deg
Line properties
R=0.0839
X=0.51833
B=0.127
P =1.624
Q=.536
V2=0.891
A2=-13.645 deg
P =.474
Q=.226
P =.45
Q=.2

## Slide 14: Execution Flow: Model Construction
Load File
Find any setup information: simulation names, definitions, libraries, basepower, etc
Read and load any imported files with no dependencies
Detect file type based on extension
Call appropriate read function
Create areas, then busses
Load any other subobjects (Links, relays, etc)
Read the simulation information (start times, actions, outputs, etc)
Load imports with dependencies
Load the solver information
Finalize and cleanup

## Slide 15: Execution Flow: Model Construction (Notes)
Busses and areas are always created ahead of other objects
All other objects should not reference other objects which are not defined ahead of it in the XML file.
Any gridSecondary or gridSubModels defined inside a parent element(XML) are created at that time the parent is created
The xml relies on the objectFactory(s) for building the correct object and uses a number of templates
Uses tinyxml as the default XML reader, tinyxml2 also available, and a json interpreter is also functional

## Slide 16: Execution Flow: States in GridDyn
Startup
Unloaded or loaded and not initialized
Initialized
Successfully completed powerflow initialization
PowerFlow Complete
Dynamic Initialized
Successfully completed dynamic initialization
Dynamic Complete
Dynamic Partial
Solver Unable to continue on its own
Halted
Not really used
May be removed
Error
Unrecoverable error
Initialize
powerflow
initialize
Dynamic
solve

## Slide 17: Execution Flow: Powerflow Initialization
Execute any events that occur before t0
Run pflowInitializeA on all objects
Setup and initialize the default solver
All objects should know how big their state information is at this point
Check the Network for issues
Call pflowInitializeB
Objects should be ready to go with a first guess

## Slide 18: Execution Flow: powerflow
makeReady()
Power Balance Loop
Flow adjustment Loop
Solve*
Guess
Check/adjust*
Do Final stuff
Measure
Adjust Gen Levels
* Will get into more detail in later

## Slide 19: Dynamic input
<?xml version="1.0" encoding="utf-8"?>
<griddyn name="2bus_test" version="0.0.1">
<bus name="bus1">
<type>SLK</type>
<angle>0</angle>
<voltage>1.05</voltage>
<generator name="gen1">
<dynmodel>typical</dynmodel>
<pmax>4</pmax>
</generator>
<load name="load1">
<P>1.15</P>
<Q>0.31</Q>
<event>@1|p=1.1</event>
</load>
</bus>
<bus name="bus2">
<load name="load2">
<P>0.45</P>
<Q>0.2</Q>
</load>
</bus>
…
…
<link from="bus1" name="bus1_to_bus2" to="bus2">
<b>0.127</b>
<r>0.0839</r>
<x>0.51833</x>
</link>
<timestop>10</timestop>
<recorder period=0.05 field="auto">
<file>twobusdynout.csv</file>
</recorder>
</griddyn>
Add a dynamic model to the generator
Add an event: change the load real power to 1.1 at time=1.0 s
Remove the powerflow only flag
-add a recorder
-add a stop time

## Slide 20: Execution
./griddynMain two_bus_dynamic_example.xml
Output on Screen
area count =0 busses=2 links= 1 gens= 1
(startup)[sim]::GridDyn version 0.28 2016-2-10
(startup)[sim]::Initializing Power flow to time -0.001000
(-0.001)[sim]::Initializing Dynamics to time 0.000000
(10)[sim]::saving recorder output:twobusdynout.csv
Simulation GridDynSimulation executed in 0.10127 seconds
simulation final Dynamic statesize= 15, 60 non zero elements in Jacobian

## Slide 21: Dynamic Results

## Slide 22: Dynamic Results

## Slide 23: Dynamic Results

## Slide 24: Execution Flow: States in GridDyn
Startup
Unloaded or loaded and not initialized
Initialized
Successfully completed powerflow initialization
PowerFlow Complete
Dynamic Initialized
Successfully completed dynamic initialization
Dynamic Complete
Dynamic Partial
Solver Unable to continue on its own
Halted
Not really used
May be removed
Error
Unrecoverable error
Initialize
powerflow
initialize
Dynamic
solve

## Slide 25: Execution Flow: Dynamic Initialization
Make sure power flow has been run and completed
Run dynInitializeA on all objects
Initialize the default dynamic solver information and set up Root finding
All objects should know the size of their dynamic state information and number of root finding functions is at this point
Call any events at time0, set up state recorders
Call pflowInitializeB
Objects should be ready to go with a first guess

## Slide 26: Execution Flow: dynamic calculation
Calculation Initial conditions
While time<timeStop
While time<next Event Time
Find next event time
Check for roots
Deal with any issues: reset if necessary*
Save state to objects
Deal with events: reset if necessary*
finalize
Solve*
* Will get into more detail later

## Slide 27: Execution Flow: Output
Power flow output
State and jacobian can output at regular intervals
Recorders to capture all sorts of properties of objects
  Binary and CSV output
  Configurable (start, stop, units)
  Saved after specified number of points or when dynamic calculations are done and time > timeStop, or when simulation is destroyed.